The handset.exe program simulates a TMX or CF1000 handset. It
defaults to COM1. The com port number may be specified as an
argument e.g.: handset 2

	To use this program you must construct an RS-232 to TTL level
translator. On the radio's DE-9S, pin 1 is TTL data in, pin 6 is TTL
data out and pins 8 and 9 are ground.
	Note that this program must be running before the radio is powered
up such that the radio can detect a "handset" on its serial port.
	The handset program is not pretty, but it should get the job
done if you don't happen to have a real handset.

   Keyboard translation:

   Due to the lack of similarity between the two layouts the following
   conventions must be observed:

   TMX              Keyboard
   Up/Down          u/d
   CL               c
   E                Shift
   RCL              r
   STO              s
   *                a      (Asterisk)
   #                o      (Octothorpe)
   0-9              0-9    (don't use keypad when shifting)
   CL-*             Ctrl-R    (reset command)